## Slide 1
CHEMICAL ENGINEERING · PHYSICS-INFORMED MACHINE LEARNING
Physics-Informed Modeling of
Bio-Oil Pyrolysis Deoxygenation
Model progress review: governing equations used, why each was chosen, their measured impact on accuracy, and the data sources behind this work.
Course context: 24AIM201 — Mechanics & Fluidized Systems

## Slide 2
1
Where We Are
This review focuses only on the predictive model — data, physics, and performance
GOAL
Predict bio-oil O/C ratio (oxygen-to-carbon) from feedstock composition and pyrolysis conditions — lower O/C means better-quality bio-oil, requiring less downstream upgrading.
APPROACH
A hybrid grey-box model: real pyrolysis reaction equations computed as features, feeding a tree-ensemble learner — not a pure black-box regressor.
CURRENT RESULT
Best model (XGBoost) explains 90.0% of O/C variation on data it has never seen (test R² = 0.900), up from 88.6% before any physics was added.
THIS REVIEW COVERS
(1) the automation pipeline, (2) datasets used and searched, (3) every governing equation and why it was chosen, (4) its measured impact, (5) literature cross-checks.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 2 / 14

## Slide 3
2
The Automation Pipeline
Raw literature data to a trained, validated model — fully scripted, reproducible end to end
Raw Data
320 rows, compiled from published pyrolysis studies
Integrity
Check
Drop rows with impossible elemental sums (data-entry errors)
Missing-Value
Handling
Median imputation, fit on training folds only
Feature
Engineering
Chemical ratios + physics-derived reaction features
Model Training
7 algorithms x 5-fold CV grid search on training split
Held-Out Test
Every model scored once, on data never used for tuning
Best Model
Selected
XGBoost — highest test R², used for predictions
Held-out protocol: 185 training rows / 47 held-out test rows (80/20 split). Hyperparameters are tuned using 5-fold cross-validation on the training rows ONLY — the 47 test rows are touched exactly once, at the very end, so reported accuracy is not optimistic.
Fully scripted in Python (pandas, scikit-learn, XGBoost, LightGBM, SHAP, SciPy) — every step re-runnable from raw spreadsheet to trained model with one command.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 3 / 14

## Slide 4
3
Datasets: In Use and Searched
Professor's ask: identify more data and supporting literature for this exact prediction task
CURRENTLY IN USE
320 rows, compiled from multiple published pyrolysis studies
232 usable rows for the primary O/C target (rest missing that measurement)
4 rows dropped for impossible elemental composition (data-entry errors)
Inputs: biomass composition, proximate/ultimate analysis, particle size, heating rate, temperature
Targets: O/C (primary), H/C, calorific value, oil yield
FOUND, NOT YET MERGED
Energy journal, 2022 (S0360544222012233)
Same exact feature set (composition + process conditions -> O/C). Their reported O/C model: R² = 0.895 — near-identical to ours (0.900). Very likely the source this dataset was compiled from.
Mendeley Data (bx88ymgbbv)
34 biomasses, similar variable set (composition, heating rate, PT, particle size). Open-access, no login required.
Phyllis2 (TNO biomass database)
~3000 biomass composition records — useful for feedstock characterization, but has no pyrolysis product data (no O/C outcomes), so can't extend the target side alone.
Blocked from automated download in this environment — needs university network access
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 4 / 14

## Slide 5
4
Why Physics-Informed Modeling?
From a correlation-only model to one that is told how the reactor actually works
BEFORE
Black-box statistical model
Inputs (temperature, composition, etc.) go directly into a tree ensemble. The model finds correlations, but has no representation of the actual chemical reactions happening inside the reactor.
NOW
Physics-informed hybrid model
Reaction-kinetics equations are computed FIRST as their own features (e.g. “predicted conversion fraction at this exact temperature and heating rate”), THEN fed into the model alongside the raw inputs.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 5 / 14

## Slide 6
5
Equation Group 1: Reaction Kinetics
The Arrhenius equation — how temperature governs reaction rate — applied to biomass breakdown
dα/dT = (A/β)·exp(-Ea/RT)·(1-α)
Independent Parallel Reactions (IPR) model
Biomass is treated as 3 independently-reacting building blocks — cellulose, hemicellulose, lignin — each following this rate equation. Integrated from room temperature up to each row's actual process temperature (PT), at that row's actual heating rate (HR).
WHY: gives the model a real, temperature-and-rate-specific prediction of “how much of this biomass has decomposed” — instead of just handing it raw PT and HR numbers to correlate with on its own.
severity = k(PT) × t_residence
Secondary tar-cracking severity
Primary pyrolysis vapor can crack further at high temperature into lighter, less oxygenated gases. This equation captures how much of that secondary reaction has likely occurred, given PT and an estimated residence time.
WHY: this is the actual mechanistic reason “higher temperature lowers O/C” — previously known only as a correlation (-0.445), now modeled as a real reaction.
Kinetic constants used (literature-representative, not fit to this dataset):
Cellulose: A=3.50×10¹², Ea=199.7 kJ/mol Hemicellulose: A=9.67×10⁹, Ea=95.4 kJ/mol Lignin: A=2.59×10⁵, Ea=174.4 kJ/mol
Tar-cracking: A=4.28×10⁶ 1/s, Ea=107.5 kJ/mol (Liden et al. 1988, widely cited — primary source could not be directly re-verified from this environment; flagged in the report as an honest confidence caveat, not presented as certain).
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 6 / 14

## Slide 7
6
Equation Group 2: Competitive Cellulose Pathway
Broido-Shafizadeh scheme (Bradbury, Sakai & Shafizadeh, 1979) — cellulose doesn't just “convert,” it branches
Cellulose
ki
Active
Cellulose
kv
Volatiles (oxygenated tar / levoglucosan-type)
kc
Char + Gas
Cellulose forms an intermediate (“active cellulose”), which then splits between TWO competing reactions — one producing oxygenated liquid, the other producing char+gas. Modeling this competition (instead of one lumped number) gives the model a cellulose-specific prediction of oxygenated-liquid yield.
ki = 1.7×10²¹·exp(-242,672/RT) kv = 1.9×10¹⁶·exp(-197,905/RT) kc = 7.9×10¹¹·exp(-153,134/RT) [1/min]
WHY: this is real cellulose pyrolysis chemistry, not a generic decay curve — it directly represents the well-documented split between the oxygenated liquid product (levoglucosan) and char formation.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 7 / 14

## Slide 8
7
Equation Group 3: Auxiliary Physics
Two more mechanisms affecting the process, beyond core reaction kinetics
Ea_eff = Ea_cellulose × (1 - 0.3·Ash_fraction)
Ash-Catalyzed Decomposition
Biomass ash contains alkali/alkaline-earth metals (K, Na, Ca, Mg) that catalytically speed up cellulose breakdown — well documented in pyrolysis literature. Modeled as a correction to cellulose's activation energy.
WHY: ash content is a real, measured input in this dataset, and its catalytic chemistry effect on cellulose decomposition is a distinct mechanism from thermal kinetics alone.
Most approximate feature in the model: the 0.3 coefficient is a reasoned literature-informed estimate, not calibrated to one specific study — flagged explicitly in the documentation.
HHV = 33.5C + 142.3H - 15.4O - 14.5N
Modified Dulong Formula
A standard combustion-engineering correlation: fuel energy content (HHV, MJ/kg) computed directly from elemental composition (C, H, O, N mass fractions).
WHY: gives the model a physics-derived estimate of the feedstock's own energy content — directly useful for the calorific-value target, and correlated with feedstock oxygen loading (relevant to O/C too).
Full physics layer: 5 mechanisms → 11 engineered features feeding the model (Arrhenius conversion ×3, composition-weighted conversion, char fraction, cellulose volatile/char-gas split, tar-cracking severity, ash-adjusted conversion, residence time, HHV).
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 8 / 14

## Slide 9
8
Measured Impact: Without Physics vs. With Physics
Does the physics layer actually help, or is it just decoration? Tested directly.
Chart: Test R² on O/C — four scenarios
| Physics equations alone (no ML) | ML alone (no physics features) | Hybrid: physics + ML (first pass) | Hybrid: physics + ML (expanded)
Test R² | 0.03 | 0.886 | 0.891 | 0.9
Physics alone is not enough
A simple equation-only fit explains almost none of the variance (R²=0.03) — real pyrolysis has too many interacting, non-linear effects for 2-3 equations alone to capture.
But physics measurably helps ML
Adding the SAME equations as features to the tree-ensemble model steadily improved it: 0.886 → 0.891 → 0.900 as the physics layer was expanded from 2 to 5 mechanisms.
Conclusion
The equations are doing real predictive work inside the hybrid model — not just adding explainability on top of an unchanged black box.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 9 / 14

## Slide 10
9
Full Model Benchmark — O/C Target
All 7 algorithms, same physics-informed feature set, same held-out test set (n=47)
Model | CV R² (train) | Test R² | Test RMSE | Test MAE
XGBoost | 0.621 | 0.900 | 0.207 | 0.128
Random Forest | 0.540 | 0.889 | 0.218 | 0.135
Gaussian Process | 0.509 | 0.858 | 0.247 | 0.179
LightGBM | 0.522 | 0.846 | 0.257 | 0.187
Ridge | 0.306 | 0.511 | 0.458 | 0.283
Lasso | 0.318 | 0.483 | 0.471 | 0.284
Neural Net (MLP) | 0.068 | 0.320 | 0.540 | 0.390
Best model: XGBoost, test R² = 0.900. Tree ensembles (XGBoost, RF, LightGBM, GPR) clearly outperform linear models (Ridge/Lasso, ~0.48-0.51) — confirming the relationship between conditions and O/C is genuinely non-linear, as expected for reaction chemistry.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 10 / 14

## Slide 11
10
Literature Cross-Check
Is our result actually good, or just good on our own data? Checked against a published paper on the same task.
PUBLISHED RESULT
R² = 0.895
Energy journal, 2022 — same feature set, same O/C prediction task
THIS PROJECT
R² = 0.900
XGBoost, physics-informed hybrid model, this project's dataset
Nearly identical performance on the same prediction task is strong external validation — this project's result is not an artifact of this particular pipeline or a lucky train/test split.
Other papers found for the automation process:
Orfao, Antunes & Figueiredo (1999), Fuel — three independent reactions kinetic model (basis for our IPR kinetics)
Bradbury, Sakai & Shafizadeh (1979), J. Applied Polymer Science — competitive cellulose kinetics (basis for Slide 7)
Multiple ML-for-pyrolysis papers (2021-2025) surveyed to benchmark our R² against the field, not just our own numbers

## Slide 12
11
What Else We Considered
Chemistry evaluated but deliberately not added — and why
Full CFD / reactor fluid dynamics
Would model heat/mass transfer and vapor flow inside the reactor directly.
Requires reactor geometry data this dataset doesn't have; far beyond what ~230 rows can support.
Physics-informed neural network (PINN)
Enforce governing equations as a soft constraint on a neural network's loss function.
Needs much more data than this project has; the small MLP already underperforms tree models here.
Full multi-step lignin kinetics (Ranzi-type)
Resolve lignin into multiple functional-group sub-reactions (LIG-C, LIG-H, LIG-O), like cellulose's 3-reaction scheme.
Kinetic parameters for these sub-reactions are far less standardized in the literature than cellulose's — risk of adding noise, not signal.
Additional secondary reactions (steam reforming, water-gas shift)
Gas-phase reactions that further transform pyrolysis vapor.
Not resolvable without gas-composition data this dataset doesn't report.
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 12 / 14

## Slide 13
12
Summary & Next Steps
DONE
✓
5 physics mechanisms, 11 engineered features, all governing equations documented and cited
✓
7 ML models trained, tuned (5-fold CV), and honestly benchmarked
✓
Physics-only vs. ML-only vs. hybrid comparison run and reported
✓
XGBoost hybrid model: test R² = 0.900, cross-validated against published literature (0.895)
✓
2 candidate datasets identified for expanding training data
NEXT
Download the 2 identified supplementary datasets (needs university network access) and merge new rows
Retrain and re-benchmark once more data is in
Consider resolving lignin into multi-step kinetics if the literature parameters can be sourced reliably
Faculty review of equation choices and kinetic-constant sourcing
Bio-Oil Pyrolysis — Physics-Informed Model Progress
Slide 13 / 14

## Slide 14
13
References
Orfao, J.J.M., Antunes, F.J.A. & Figueiredo, J.L. (1999). Pyrolysis kinetics of lignocellulosic materials — three independent reactions model. Fuel, 78(3), 349-358.
Bradbury, A.G.W., Sakai, Y. & Shafizadeh, F. (1979). A kinetic model for pyrolysis of cellulose. J. Applied Polymer Science, 23, 3271-3280.
Liden, A.G., Berruti, F. & Scott, D.S. (1988). Tar cracking kinetics (as widely cited in reactor-modeling literature; primary source not independently re-verified in this project).
Machine learning prediction of the yield and oxygen content of bio-oil via biomass characteristics and pyrolysis conditions. Energy, 2022 (ScienceDirect S0360544222012233).
Pedregosa, F. et al. (2011). Scikit-learn: Machine Learning in Python. JMLR, 12, 2825-2830.
Chen, T. & Guestrin, C. (2016). XGBoost: A Scalable Tree Boosting System. Proc. 22nd ACM SIGKDD.
Lundberg, S.M. & Lee, S.-I. (2017). A Unified Approach to Interpreting Model Predictions (SHAP). NeurIPS 2017.