## Slide 1: Physics-Aware Machine Learning for Bio-Oil Pyrolysis
More bio-oil, less oxygen
Umasuthan Palaniappan (CB.AI.U4AIM25041)
24AIM201 Mechanics and Fluidized Systems | Guide: Dr. Akhil Mohan | Amrita Vishwa Vidyapeetham
Notes: This project uses machine learning with physics to help make more bio-oil with less oxygen.

## Slide 2: The goal: better bio-oil, so separation is easier
Biomass
Pyrolysis
Bio-oil
Separation
We predict
How much oil we get, and how much oxygen is in it (less oxygen = better fuel).
The problem
Many ML models look accurate but fail on new biomass, and they ignore physics.
Notes: Biomass is heated to make bio-oil, which Dr. Mohan's work then separates. We predict how much oil we get and how much oxygen it has. The problem is that many models look good on paper but fail on new biomass.

## Slide 3: What we did
Cleaned the data
Found the same biomass repeated many times.
651 → 118
real biomasses
Tested honestly
Only on biomass the model had never seen.
0.66 → −0.18
accuracy drop (yield)
Added physics
Heat transfer, reaction rates, chemistry.
Better
and follows real trends
Notes: First we cleaned two public datasets and found that 651 apparent biomasses were really 118. Then we tested honestly, only on unseen biomass, and the usual accuracy dropped sharply. Finally, adding physics made the models better and made them follow real trends, like best oil around 525 degrees.

## Slide 4: The result: a Pyrolysis Advisor
You enter
Biomass type and particle size
It tries
156 reactor settings
It recommends
480 °C
at 300 °C/min
Found the right best temperature for 2 of 3 new biomasses
1 to 2 real experiments cut the error from 8.3% to 4.2%
Warns when a biomass is too unfamiliar
Notes: The advisor takes a biomass, tests 156 reactor settings and recommends the best balance of high oil and low oxygen. For pine wood: 480 degrees at 300 degrees per minute. It was right for two of three unseen biomasses, gets much more accurate with one or two real experiments, and warns when it is unsure.

## Slide 5: Conclusion
Honest testing shows many ML scores are overstated
Physics makes the models better and sensible
The advisor suggests settings for more oil, less oxygen
Less oxygen means easier separation (Dr. Mohan’s work)
Thank you | Questions?
Notes: To sum up: honest testing, physics-aware models, and a practical advisor that helps produce better oil for separation. Thank you.